## Slide 1
contributions by Tommaso Bonato, Daniele De Sensi, Salvatore Di Girolamo, Shigang Li, Marco Heddes, Jon Belk, Deepak Goel,
Miguel Castro, Steve Scott, Thomas Haener, Matthias Troyer Tal Ben-Nun, Alexandros Ziogas, Johannes de Fine Licht, Tiziano de Matteis, Timo Schneider, Andreas Kuster, Manuel Burger, Philip Schaad, Dominic Hofer and the whole DAPP team @ SPCL
“A painting of Gdansk”
Post-Moore spatial computing: from chips to clusters. Torsten Hoefler Keynote at 14th International Conference on Parallel Processing and Applied Mathematics Sept. 2022, Gdansk, Poland

## Slide 2: Changing hardware constraints and the physics of computing
1nm
[1]: Marc Horowitz, Computing’s Energy Problem (and what we can do about it), ISSC 2014, plenary
[2]: Moore: Landauer Limit Demonstrated, IEEE Spectrum 2012
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
0.9 V [1]
32-bit FP ADD: 0.9 pJ
32-bit FP MUL: 3.2 pJ
2x32 bit from L1 (8 kiB): 10 pJ
2x32 bit from L2 (1 MiB): 100 pJ
2x32 bit from DRAM: 1.3 nJ
…
5nm
2nm
Landauer limit 3 * 10-21 (32-bit FP, >0.2*10-6 pJ)
Electrical data movement:
loss ~ resistancy * length / cross-section-area
Three key aspects of silicon scaling over the last four decades
            Shrinking feature size
            Tighter integration of units
            Smaller distances
Passing away with Moore’s law
(at the nano-/transistor-level)
Continued design for integration
(at the package/node/system-levels)
Notes: Mark Horowitz talk: https://www.youtube.com/watch?v=7gGnRGko3go
45nm, 0.9V  32bit FADD: 0.9pJ, FMUL: 3.7pJ, 2 operand (64bit) load from L1 (8kiB): 10pJ, from L2 (1MiB): 100pJ, from DRAM: 1.3-2.6nJ [1]
FP computation approaches Landauer limit (3e-21 J) [2]
  Assuming all bits are switched in 32 bit FP, ~0.2aJ (atto Joules = 10e-6pJ)
Electrical data movement suffers from resistance
  Heat loss: ~ resistancy * length / cross-section-area
 process shrinkage benefits computation energy but increases communication energy

## Slide 3: Beyond Moore’s Law - Design for integration
TSVs bring DRAM memory and compute closer
NUMA vs. UMA in an interesting design space
3d integration
Interposer connects chiplets for flexibility + cost saving per package
Simple topologies today, developing
  cf. SlimNOC [1]
chiplets
C2C links with PCB or flyover cables
cf. NVIDIA DGX-station
    4xA100 on board
boards
Flyover or local copper cables
e.g., Dragonfly groups
cf. DGX-2 (16xA100)
“the world’s largest GPU”
nodes
Local electrical or global optical cables
  Fat Tree, Dragonfly, Slim Fly (optimal)
Workload specialization
clusters
Those are free but have very limited connectivity
Very short electrical is cheap, long fiber very expensive!
challenges: cooling and inexpensive connectivity
Design AI-specialized
networks!
M. Besta et al.: Slim NoC: A Low-Diameter On-Chip Network Topology for High Energy Efficiency and Scalability, ASPLOS 2018
Notes: Mark Horowitz talk: https://www.youtube.com/watch?v=7gGnRGko3go
45nm, 0.9V  32bit FADD: 0.9pJ, FMUL: 3.7pJ, 2 operand (64bit) load from L1 (8kiB): 10pJ, from L2 (1MiB): 100pJ, from DRAM: 1.3-2.6nJ [1]
FP computation approaches Landauer limit (3e-21 J) [2]
  Assuming all bits are switched in 32 bit FP, ~0.2aJ (atto Joules = 10e-6pJ)
Electrical data movement suffers from resistance
  Heat loss: ~ resistancy * length / cross-section-area
 process shrinkage benefits computation energy but increases communication energy

## Slide 4: Modern Deep Learning Workloads
f(x)
layer-wise weight update
  GPT-3: 96 (complex) layers
    175 bn parameters (700 GiB in fp32)
    2048-token “sentences”
  GPT-3: 30-50k dictionaries
  takes weeks to train
A robot may __ injure a human being or, through inaction, allow a human being to come to harm.
…
0.74
0.28
0.02
0.07
0.33
0.04
0.02
not
sometimes
always
house
never
and
boat
1.00
0.00
0.00
0.00
0.00
0.00
0.00
not
sometimes
always
house
never
and
boat
10k GPUs
T. Ben-Nun, TH: Demystifying parallel and distributed deep learning: An in-depth concurrency analysis, ACM Computing Surveys (CSUR), 2019
  GPT-3: 500 billion tokens
  ImageNet (22k): A few TB
  Soon: the whole internet!

## Slide 5: Academia and research are catching up fast!

## Slide 6: Data parallelism – limited by batch-size
Simple and efficient solution, very easy to implement
Duplicate parameters at all processors (d’oh memory is expensive and scarce!)
…
…
…
T. Ben-Nun, TH: Demystifying parallel and distributed deep learning: An in-depth concurrency analysis, ACM Computing Surveys (CSUR), 2019
minibatch 1
minibatch 2
minibatch 3
minibatch 4

## Slide 7: Pipeline parallelism – limited by number of layers
Layers/parameters can be distributed across processors
Sparse communication pattern (only pipeline stages)
Mini-batch has to be copied through all processors and latency doesn’t decrease!
…
T. Ben-Nun, TH: Demystifying parallel and distributed deep learning: An in-depth concurrency analysis, ACM Computing Surveys (CSUR), 2019
minibatch 1
minibatch 2
minibatch 3
minibatch 4

## Slide 8: Operator parallelism – limited by operator or layer size
Parameters can be distributed across processors
Mini-batch has to be copied to all processors
Forward and backward requires extremely high communication (cut MMMs)
T. Ben-Nun, TH: Demystifying parallel and distributed deep learning: An in-depth concurrency analysis, ACM Computing Surveys (CSUR), 2019
…
1
…
3
minibatch 1
minibatch 2
minibatch 3
minibatch 4
Notes: - Htor: discuss - all-to-all even for conv and pooling???

## Slide 9: “3D” Hybrid parallelism
T. Ben-Nun, T. Hoefler: Demystifying Parallel and Distributed Deep Learning: An In-Depth Concurrency Analysis, arXiv Feb 2018
Layers/parameters can be distributed across processors
Can distribute minibatch
Often specific to layer-types (e.g., distribute fc layers but handle conv layers data-parallel)
  Enables arbitrary combinations of data, model, and pipeline parallelism – very powerful!
Operator Parallelism
Data Parallelism
Pipeline Parallelism
minibatch 1
minibatch 2
minibatch 3
minibatch 4
…
…
…
Notes: Should we add the survey here as mentioning all of them together?
  [tal] Done

## Slide 10: Communication characteristics of 3D parallelism in Deep Learning
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, SC22
1
2
D
allreduce ring
communication
1
2
P
allreduce ring or neighbor communication
1
2
O
1,1,D
2,1,1
3,1,1
1,2,D
2,2,1
3,2,1
1,P,D
2,P,D
O,P,D
1,1,2
2,1,1
3,1,1
1,2,2
2,2,1
3,2,1
1,P,2
2,P,2
O,P,2
1,1,1
2,1,1
O,1,1
2,2,1
O,2,1
2,P,1
O,P,1
1,2,1
1,P,1
3D - Data, Pipeline, and Operator Parallelism
Can be overlapped
Can be overlapped
Can not be overlapped
Data Parallelism
Operator Parallelism
Pipeline Parallelism
Communication is (largely) a logical 3D Torus

## Slide 11: (Network and memory) bandwidth is the new oil in AI supercomputing
Memory bandwidth can be satisfied using HBM3 and friends
  Technologies are quickly becoming available
Network bandwidth is more complex and requires full-system and packaging tricks
HPC:
  Slingshot (‘21): 200G per GPU
  InfiniBand CX-7 (‘22): 400G per NIC
AI:
  Google TPUv2 (‘21): 1T
  AWS Trainium (‘21): 1.6T
  DGX-2 (A100, ‘21): 4.8T (islands of NVLINK)
  Tesla Dojo (‘22): 128T  Broadcom TH5 / NVIDIA Spectrum 4: 51.2T
Performance models indicate even higher demands
  Massive transformer EDAGs have really bad cuts
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, to appear at SC22 and arXiv (today?)
640x
“AI system entangled in cables”
A fat tree with 16k accelerators and 1.6T would cost $680M!
  
Conventional HPC topologies may be unaffordable for AI bandwidths!

## Slide 12: Co-designing an AI supercomputer with unprecedented and cheap bandwidth
y,1
y,2
y,3
y,x
1,1
1,2
1,3
1,x
2,1
2,2
2,3
2,x
3,1
3,2
3,3
3,x
…
…
…
…
…
…
…
…
…
N1
N2
N3
N4
S1
S2
S3
S4
W1
W2
W3
W4
E1
E2
E3
E4
four directions
per plane (N,S,E,W)
four planes
per accelerator
axb accelerators
per board
4x4 board
inexpensive short
PCB connections
on board
each plane fully-connected in x
accelerator
package
2x2
board
packet
switch
each plane fully-connected in y
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, to appear at SC22 and arXiv (today?)

## Slide 13: A bandwidth-cost-flexibility tradeoffs
Global Topology
(e.g., Fat Tree)
HammingMesh
(many configurations)
Local Topology
(e.g., 2D Torus)
(large) reduce bandwidth
placement flexibility
injection bandwidth
global bandwidth
-
-
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, to appear at SC22 and arXiv (today?)

## Slide 14: HammingMesh cost vs. bandwidth – simulated using SST (0.6M core hours)
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, to appear at SC22 and arXiv (today?)
“an AI coin”
Single switch per row/column

## Slide 15: Full network simulations (using SST with MPI-style driver)
TH et. al.: HammingMesh: A Network Topology for Large-Scale Deep Learning, to appear at SC22 and arXiv (today?)
Network is always cheaper, needs to be weighed against full system cost!

## Slide 16: Changing hardware constraints and the physics of computing
1nm
[1]: Marc Horowitz, Computing’s Energy Problem (and what we can do about it), ISSC 2014, plenary
[2]: Moore: Landauer Limit Demonstrated, IEEE Spectrum 2012
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
0.9 V [1]
32-bit FP ADD: 0.9 pJ
32-bit FP MUL: 3.2 pJ
2x32 bit from L1 (8 kiB): 10 pJ
2x32 bit from L2 (1 MiB): 100 pJ
2x32 bit from DRAM: 1.3 nJ
…
5nm
2nm
Landauer limit 3 * 10-21 (32-bit FP, >0.2*10-6 pJ)
Electrical data movement:
loss ~ resistancy * length / cross-section-area
Back to our three key aspects of silicon scaling over the last four decades
                Shrinking feature size
                Tighter integration of units
                Smaller distances
Passing away with Moore’s law
(at the nano-/transistor-level)
Continued design for integration
(at the package/node/system-levels)
Programming spatial devices
(at all levels)
16
How can we achieve this?
Notes: Mark Horowitz talk: https://www.youtube.com/watch?v=7gGnRGko3go
45nm, 0.9V  32bit FADD: 0.9pJ, FMUL: 3.7pJ, 2 operand (64bit) load from L1 (8kiB): 10pJ, from L2 (1MiB): 100pJ, from DRAM: 1.3-2.6nJ [1]
FP computation approaches Landauer limit (3e-21 J) [2]
  Assuming all bits are switched in 32 bit FP, ~0.2aJ (atto Joules = 10e-6pJ)
Electrical data movement suffers from resistance
  Heat loss: ~ resistancy * length / cross-section-area
 process shrinkage benefits computation energy but increases communication energy

## Slide 17: Beyond Moore’s Law – Towards spatial programming
MPI, OpenMP, CUDA, …
Principles:
  Work/Depth
  Compute Tasks
  Temporal scheduling
  Temporal locality
Procedural reasoning (this then that)!
Temporal parallel programming
RTL, HLS, …
Principles:
  Pipelining
  Dataflow / data movement
  Spatiotemporal scheduling
  Spatial locality
Spatial thinking (this here, that there)!
Spatial parallel programming
Zooming in …
We know this since decades!
Notes: Mark Horowitz talk: https://www.youtube.com/watch?v=7gGnRGko3go
45nm, 0.9V  32bit FADD: 0.9pJ, FMUL: 3.7pJ, 2 operand (64bit) load from L1 (8kiB): 10pJ, from L2 (1MiB): 100pJ, from DRAM: 1.3-2.6nJ [1]
FP computation approaches Landauer limit (3e-21 J) [2]
  Assuming all bits are switched in 32 bit FP, ~0.2aJ (atto Joules = 10e-6pJ)
Electrical data movement suffers from resistance
  Heat loss: ~ resistancy * length / cross-section-area
 process shrinkage benefits computation energy but increases communication energy

## Slide 18: Writing fast spatial programs for FPGAs and CGRAs (in productive HLS)
Welcome to #pragma hell!

## Slide 19: Beyond Moore’s Law – Towards spatial programming
MPI, OpenMP, CUDA, …
Principles:
  Work/Depth
  Compute Tasks
  Temporal scheduling
  Temporal locality
Procedural reasoning (this than that)!
Temporal parallel programming
RTL, HLS, …
Principles:
  Pipelining
  Dataflow / data movement
  Spatiotemporal scheduling
  Spatial locality
Spatial thinking (this here, that there)!
Spatial parallel programming
Temporal algorithms
Spatial optimizations
Data-Centric Intermediate Representation (DCIR)
Data Centric Python (DaCe)
Relatively simple !
Very hard
(for me) !
Notes: - Is spatial strictly harder than temporal? They’re both NP complete?

## Slide 20: Upleveling programming in the 21st century – Performance Portability
Parametric Dataflow
Graphs (SDFG)
Graph Transformations
(API, Interactive)
Transformed
Dataflow
Performance
Results
C++ code generation/runtime
*
*
*
*
*
*
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19
Domain Scientist
DSLs
SDFG Builder API
Multi-Level
Library Nodes
Applied Scientist
translate DSL into
parametric dataflow graphs
Performance Engineer
Specialized
Code Generation
CPU Code
GPU Code
FPGA Code
Runtime
10s of SLOC
1000s of auto-generated SLOC
100s of reusable SLOC

## Slide 21: All about the IR – DaCe translates to Parametric Dataflow Graphs (SDFGs)
Tasklet
Memlets
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19

## Slide 22: Data-Parallelism in Parametric Dataflow Graphs (SDFGs)
…
B
Tasklet
A[1]
B[1]
A[0]
B[0]
A[N-1]
B[N-1]
A
Tasklet
Tasklet
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19

## Slide 23: Data-Parallelism in Parametric Dataflow Graphs (SDFGs)
A
B
[i=0:N]
Tasklet
A[i]
B[i]
[i=0:N]
A[0:N]
B[0:N]
…
B
Tasklet
Tasklet
Tasklet
A[1]
B[1]
A[0]
B[0]
A[N-1]
B[N-1]
A
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19
Iteration space (map)

## Slide 24: States in Parametric Dataflow Graphs (SDFGs)
A
B
[i=0:N]
Tasklet
A[i]
B[i]
[i=0:N]
A[0:N]
B[0:N]
C
A
[i=0:N]
Tasklet
C[i]
A[i]
[i=0:N]
C[0:N]
A[0:N]
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19

## Slide 25: States in Parametric Dataflow Graphs (SDFGs)
State s1
State s0
A
B
[i=0:N]
Tasklet
A[i]
B[i]
[i=0:N]
A[0:N]
B[0:N]
C
A
[i=0:N]
Tasklet
C[i]
A[i]
[i=0:N]
C[0:N]
A[0:N]
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19

## Slide 26: Parametric Dataflow Graphs - Concepts
Store volatile (buffers, queues, RAM) and nonvolatile (files, I/O) information
Can be sources or sinks of data
Stateless functions that perform computations at any granularity
Data access only through ports
Data flowing between containers and tasklets/ports
Implemented as access, copies, streaming, …
Map scopes provide parallelism
States constrain parallelism outside of datatflow
Data Containers
Computation
Data Movement / Dependencies
Parallelism and States
Ben-Nun, de Fine Licht, Ziogas, TH: Stateful Dataflow Multigraphs: A Data-Centric Model for High-Performance Parallel Programs, SC19

## Slide 27: Generating spatial hardware descriptions
Stateful DataFlow multiGraph (SDFG)
Graph Transformations
*
*
*
*
*
*
All data movement is explicit
for (int n0 = 0; n0 < (N / P); n0 += 1) {
dace::vec<float, 4> C_buffer[(M / 4)];
for (int k = 0; k < K; k += 1) {
float A_reg;
for (int n1 = 0; n1 < P; n1 += 1) {
#pragma HLS PIPELINE II=1
#pragma HLS LOOP_FLATTEN
{
float a_in = (A_pipe[p]).pop();
///////////////////
// Tasklet code (buffer_a)
if ((n1 == ((P - p) - 1))) {
A_reg = a_in;
}
if ((p < (P - 1))) {
A_pipe[(p + 1)].push(a_in);
}
///////////////////
}
}
for (int m = 0; m < (M / 4); m += 1) {
#pragma HLS PIPELINE II=1
#pragma HLS LOOP_FLATTEN
{
float a_in = A_reg;
dace::vec<float, 4> b_in = (B_pipe[p]).pop();
dace::vec<float, 4> c_in = C_buffer[m];
...
Code generated for CPU, GPU, FPGA.
Pure dataflow sections.
Fluent mapping to spatial architectures!
Parametric Dataflow
Graphs (SDFG)
Performance Engineer
de Fine Licht et al.: Transformations of High-Level Synthesis Codes for High-Performance Computing IEEE Transactions on Parallel and Distributed Systems (TPDS). 2021

## Slide 28
…
Code generation
for (int n0 = 0; n0 < (N / P); n0 += 1) {
dace::vec<float, 4> C_buffer[(M / 4)];
for (int k = 0; k < K; k += 1) {
float A_reg;
for (int n1 = 0; n1 < P; n1 += 1) {
#pragma HLS PIPELINE II=1
#pragma HLS LOOP_FLATTEN
{
float a_in = (A_pipe[p]).pop();
///////////////////
// Tasklet code (buffer_a)
if ((n1 == ((P - p) - 1))) {
A_reg = a_in;
}
if ((p < (P - 1))) {
A_pipe[(p + 1)].push(a_in);
}
///////////////////
}
}
for (int m = 0; m < (M / 4); m += 1) {
#pragma HLS PIPELINE II=1
#pragma HLS LOOP_FLATTEN
{
float a_in = A_reg;
dace::vec<float, 4> b_in = (B_pipe[p]).pop();
dace::vec<float, 4> c_in = C_buffer[m];
...
Xilinx Vivado HLS
Intel OpenCL
for (int n0 = 0; n0 < (N / P); n0 += 1) {
float4 C_buffer[(M / 4)];
#pragma ivdep
for (int k = 0; k < K; k += 1) {
float A_reg;
#pragma loop_coalesce
for (int n1 = 0; n1 < P; n1 += 1) {
float a_in = read_channel_intel(A_pipe[p]);
float *a_reg = &A_reg;
#define a_out A_pipe[(p + 1)] // God save us
///////////////////
// Tasklet code (buffer_a)
if ((n1 == ((P - p) - 1))) {
*a_reg = a_in;
}
if ((p < (P - 1))) {
write_channel_intel(a_out, a_in);
}
///////////////////
#undef a_out
}
#pragma loop_coalesce
#pragma ivdep
for (int m = 0; m < (M / 4); m += 1) {
float a_in = A_reg;
float4 b_in = read_channel_intel(B_pipe[p]);
float4 c_in = C_buffer[m]; ...
Cross-vendor support
de Fine Licht et al.: Transformations of High-Level Synthesis Codes for High-Performance Computing IEEE Transactions on Parallel and Distributed Systems (TPDS). 2021

## Slide 29
…
Code generation
N = dace.symbol("N")
K = dace.symbol("K")
M = dace.symbol("M")
P = dace.symbol("P")
W = dace.symbol("W")
def make_sdfg():
# ...do stuff...
return sdfg
if __name__ == "__main__":
P.set(8) # 8 processing elements
W.set(4) # 4-way vectorization
# Matrix of size 1024x1024x1024
M.set(1024)
K.set(1024)
N.set(1024)
gemm = make_sdfg()
# Initialize arrays: Randomize A and B, zero C
A = np.ndarray([N.get(), K.get()], dtype=np.float32)
B = np.ndarray([K.get(), M.get()], dtype=np.float32)
C = np.ndarray([N.get(), M.get()], dtype=np.float32)
A[:] = np.random.rand(N.get(), K.get()).astype(np.float32)
B[:] = np.random.rand(K.get(), M.get()).astype(np.float32)
C[:] = np.random.rand(N.get(), M.get()).astype(np.float32)
gemm(A=A, B=B, C=C, N=N, K=K) # M is fixed at compile-time
DaCe programs are exposed as Python functions
Interfaces with NumPy arrays
SDFGs defined or loaded using Python API
DaCe successfully runs 30/30 Polybench applications directly from NumPy (Xilinx + Intel)!

## Slide 30
Visual Studio Code integration Plugin "DaCe SDFG Viewer (SDFV)"

## Slide 33: Case study: Weather simulation at MeteoSwiss
Weather service is currently GPU-powered [2]
[1] Institute for Atmospheric and Climate Science and Computer Graphics Laboratory, ETH Zürich [https://vimeo.com/389292423]
[1]
[2] Swiss National Supercomputing Center (CSCS) [https://www.cscs.ch/computers/arolla-tsa-meteoswiss]

## Slide 34: Weather stencil programs
Idea: Pipeline dependencies in a fine-grained manner on a spatial computing architecture.
Gysi et al.: MODESTO: Data-centric Analytic Optimization of Complex Stencil Programs on Heterogeneous Architectures, 29th International Conference on Supercomputing (ICS'15)

## Slide 35: StencilFlow
Map the entire stencil program to a fully-pipelined parallel streaming hardware architecture.
Transparently expose this mapping from a high-level scientific DSL.
Gysi et al.: MODESTO: Data-centric Analytic Optimization of Complex Stencil Programs on Heterogeneous Architectures, 29th International Conference on Supercomputing (ICS'15)

## Slide 36: Taming the weather
We can now generate and process the stencil DAG.
Performs 130 floating point operations per grid point (including sqrt, min, and max operations).
20 data-dependent branches
Arithmetic intensity of 65/18 Op/Byte.
de Fine Licht et al.: StencilFlow: Mapping Large Stencil Programs to Distributed Spatial Computing Systems 19th ACM/IEEE International Symposium on Code Generation and Optimization (CGO'21), 2021

## Slide 37: Taming the weather
The Stratix 10 is held back by insufficient bandwidth.
FPGAs are good at deterministically exploiting bandwidth, but require a lot of pipeline parallelism.
CPU and GPU results are highly optimized codes produced by the DAWN framework [1].
[1] Osuna et al.: Dawn: a High Level Domain-Specific Language Compiler Toolchain for Weather and Climate Applications, Supercomputing Frontiers and Innovation 2020
all memory bound
318 MHz at 48% DSP utilization

## Slide 38: aCe is a versatile platform
DaCeML
(PyTorch/ONNX)
C
(C99)
Fortran
(in planning)
GridTools
(Weather & Climate)
Your favorite language/DSL
(through SDFG builder)
NVIDIA GPU
AMD GPU
x86 CPU
Intel FPGA
Xilinx AMD FPGA
RTL
(soon)
NumPy
ARM SVE
Your favorite processor
(through C++ codegen)
Ben-Nun et al. "Stateful dataflow multigraphs: A data-centric model for performance portability on heterogeneous architectures." Supercomputing 2019 (SC'19).

## Slide 39: Last example: Gordon Bell Prize 2019 on ORNL’s Summit (Top-1 Machine)
pip install dace
Gordon Bell Prize 2019
  Quantum Nano Transport simulation
    Design of future micro- processors
Now working on large-scale:
  Deep Learning (transformers)
  Climate (COSMO, icon, fv3)
  Green’s functions solvers
  … your project?
http://spcl.inf.ethz.ch/DAPP

## Slide 40: Overview and wrap-up
This project has received funding from the European Research Council (ERC) under grant agreements "DAPP and PSAP (PI: T. Hoefler)".
https://www.youtube.com/c/ScalableParallelComputingLabETHZurich
Future hardware must be spatial!
Spatial reasoning is too hard!
Combine temporal algorithms and spatial optimizations!
We need effective
tool support!
DaCe offers ideas for spatial design
Early results
Look promising
Modularity will
be important!

## Slide 41: Coming soon: Mapping Deep Learning Codes to FPGAs and CGRAs
Rausch et al. “A Data-Centric Optimization Framework for Machine Learning”, in ICS’22
Key principle: minimize data movement and optimize data layout
MLSys’20

## Slide 42: Another observation: modularity of frequency
Despite all data-movement optimizations, our frequencies were far from the target (often <200 MHz)
int i, k;
for(i=0; i<k; ++i)
n += n*obj;
k = n*n
int i, k;
for(i=0; i<k; ++i)
n += n*obj;
k = n*n
int i, k;
for(i=0; i<k; ++i)
n += n*obj;
k = n*n

## Slide 43: A little trick: temporal vectorization aka. automatic multi-pumping
[1] Johnsen et al.: Temporal Vectorization: A Compiler Approach to Automatic Multi-Pumping, ICCAD 2022

## Slide 44: How can temporal vectorization be implemented?
[1] Johnsen et al.: Temporal Vectorization: A Compiler Approach to Automatic Multi-Pumping, ICCAD 2022

## Slide 45: Performance of temporal vectorization on a Xilinx AMD Alveo U280
Matrix Multiplication
Jacobi 3D stencil
Diffusion 3D stencil
[1] Johnsen et al.: Temporal Vectorization: A Compiler Approach to Automatic Multi-Pumping, ICCAD 2022
Hand-optimized comm-avoiding.
Standard HLS
Temporal vectorization
Nearly 2x frequency increase due to shorter paths (modularity) mapping