## Slide 1: Neuromorphic Computing
Suma George Cardwell, PhD
Towards Brain-like Energy Efficiency
SAND 2024-11671C
Principal Member of Technical Staff
Sandia National Laboratories, USA
Parallel Processing and Applied Mathematics (PPAM) 2024
Ostrava, Czech Republic
September 9th, 2024

## Slide 2: MODERN COMPUTING LANDSCAPE
DIGITAL COMPUTING
ANALOG COMPUTING
Discrete-valued
Deterministic
High-Precision
Simple(r) building blocks
Continuous-valued
Stochastic
Lower-Precision
Complex building blocks (neurons)
CPU, GPU, FPGA
Brain , FPAA
FPAA: Field Programmable Analog Array
FPGA: Field Programmable Digital Array
Notes: this is paradigm shift. I want to challenge you to think differently

## Slide 3: SINGLE NEURON COMPLEXITY
Biological Neurons have rich dynamics
Size
Single Neuron Biological Complexity
(Nonlinear Dynamics, Learnable parameters, etc.)
Perceptron
x1
x2
x3
y
Z
Activation Function
Inputs
Output
Leaky Integrate and Fire
Hodgkin Huxley Neuron

## Slide 4: ENERGY CONSUMPTION OF MODERN AI SYSTEMS
1T
1000 T
175 B
Neuromorphic Computing gives a path forward for power efficiency scaling and meeting future computing needs.
Notes: We compare multiple large language model's training and inference metrics and compare to human energy consumption over report life expectancy in the US (73.6 Years, 2500 calories per day for Men and 79.1 years, 2000 calories for women). 175 Billion parameters- GPT-3 1M KWh, on average humans with 1000 T parameters- two orders of magnitude less.

## Slide 5: NEUROMORPHIC COMPUTING
Functionality
Solves ill-structured problems with little training
Online learning/ Continual Learning
Transfer learning
Attributes
Computational Memory/In-memory computing
More complexity and computation/ single unit
Self-organizing/ Reconfigurable
Spiking/event-driven communication
Sub-threshold computation
Stochasticity as a feature
Dense local connectivity
Massively parallel computation
TAKING INSPIRATION FROM BRAINS
1MMAC/(s)/pW
1MMAC/(s)/mW
Single Neuron
Average CPU
Human Brain
Hasler 2016
MMAC: Million Multiply Accumulates
Notes: what brains can do vs. how they do it.
add a slide for complexity--different neurons

## Slide 6: Neuromorphic COMPUTING APPROACHES
Varied solutions proposed spanning digital, mixed-signal and beyond-CMOS
DIGITAL CMOS
ANALOG/ MIXED-SIGNAL CMOS
CPU, NPU, FPGA
NVM, Analog, Sub-threshold
BEYOND-CMOS
Memristors, FeFETs, MTJs etc.
Scaled to 1.15 B/ 2B neurons
Deterministic
High-Precision
Scaled to 1 M
Analog/ Stochastic
Low-Precision
In-memory computing
Analog/ Stochastic
Low-precision
Integration with CMOS

## Slide 7: Neuromorphic BUILDING BLOCKS
Neuromorphic offers computational richness
In-memory Computing
With Synapses
Sensory Processing
Silicon Retina/ Event Sensor
Silicon Cochlea etc.
Scientific
Computing
AI/ML
(ANN, SNN)
Brain-Inspired Algorithms
Edge
Computing
High Performance Computing
Neural Processing
Dendrites, Learning, Multi-modal
APPLICATIONS

## Slide 8: NEUROMORPHIC SUPERCOMPUTER
Neuromorphic systems with billions of neurons
SNL hosts Intel’s Hala Point, which utilizes the Loihi 2 chips to realize one of the largest neuromorphic supercomputers in the world.
1.15 Billion neurons and trillions of synapses with a total power consumption of only 2600 W
The Hala Point system incorporates 1,152 Loihi 2 processors, each of which can simulate a million neurons.
Capable of 15 TOPS-per-watt at 8-bit precision and does not require extensive data-processing or batching in advance.

## Slide 9: NEUROMORPHIC COMPUTING FOR PERFORMANCE
Key attributes we need:
Leverage stochasticity as a feature
Scalability and Complexity
Codesign across scales
Software tools for Codesign
Application specific Solutions
Design of Heterogeneous Architectures
Next-generation Neuromorphic Architectures for HPC and Edge
BRAINS
AI/ML with
CONVENTIONAL
DIGITAL
Less Power
More Computation
NEUROMORPHIC
COMPUTING
Cardwell et al., Neuromorphic IOP 2024
Under Review

## Slide 10: OPPORTUNITIES IN NEUROMORPHIC COMPUTING

## Slide 11: SCALABILITY VS. COMPLEXITY
We need to increase computational efficiency as well as computational density for neuromorphic systems.
We can improve the complexity of a single neuron.
Novel devices and materials can help bridge this gap but codesign is a challenge.
NEUROMORPHIC COMPUTING NEEDS BOTH!
Scalability (# of Neurons)
Intel Loihi
100 Million neurons
IBM TrueNorth
1 Million
NeuroGrid
1 Million Neurons
Dragonfly Brain
1 Million Neurons
Mouse Brain
100 Million Neurons
Human Brain
(100 Billion)
Biological Complexity
(Nonlinear Dynamics, Learnable parameters, etc.)
GT Neuron, 21 HH
with dendrites
Intel Hala Point
(Loihi 2)
1.15 Billion neurons
Biological neurons have rich dynamics and a lot more computational power.

## Slide 12: DENDRITES IMPROVE COMPUTATION WITHIN A SINGLE NEURON
SIMPLE NEURONS
Simpler neuron models requires larger neural networks.
  Power hungry ANNs
  Inefficient scaling
  Inefficient hardware implementations
  Focus only on synapses and
COMPLEX NEURONS
Active Dendrites improves performance of Artificial Neural Networks
  More energy efficiency (“Neural Network within a neuron”), non-linear filtering
  Heterogeneity
  More computations/unit
  Better Connectivity and fan-in (3D architectures)
  Scalable with CMOS+X approaches.
Plastic Synapses
Learning Mechanisms
  Our Current Research
  Dendrites supporting shunting Inhibition
    Pattern Recognition (NICE 2023, ICONS 2023)
    Direction-Selective (ICONS 2024)
  Software library for analog hardware-based dendrites (NeurIPS workshop, NICE 2023)
  DEND-NET: SNN with dendrites (Neuro IOP 2024 -In Review)
  Neuromorphic Design Space Exploration with SANA-FE tool in collaboration with UT Austin.
Synaptic Inputs
Raxial
Rleak
Cleak
Vmembrane
w1
w2
w3
DENDRITE CABLE
Analog devices and circuits well suited to model dendrites efficiently in hardware.

## Slide 13: COMPUTATION USING THE DENDRITES
Over 70% of the neuron’s volume (Stuart 2016)
Great diversity of dendrites within a single brain and across animal species.
Insights from neuroscience are foundational to the pursuits of neuromorphic computing.
Biological dendrites are known for their complex physical structures that incorporate significant fan-in (~10,000 inputs).
Dendrites are not just wires!
Segev, Nature 1998
Notes: A) Traces of dragonfly TSDN MDT5 dendrites [44]. (B)Trace of a layer 5 (L5) pyramidal neuron with basal and apical dendrites.Image (A) reproduced courtesy Dr. Paloma Gonzalez-Bellido. Image (B) courtesy of Dr. Hysell Oviedo, Department of Neuroscience, Washington University School of Medicine in St. Louis, USA.

## Slide 14: DENDRITIC TOOLKIT FOR COMPUTATION
Dendrites are not just wires!
They can perform interesting computation like:
  Coincidence Detection
  Current Summation
  Directional selectivity
  Non-linear filtering
  Amplification of Synaptic inputs
Dendrites are tree-like structures that connect neurons synapses to its soma.
London 2005, Poirazi 2020
Increased Connectivity and Computation
Rleak
Cleak
Vmem
Raxial
Cleak
Rleak
Vmem
Vleak
Vaxial
Dendrites using Transistors
Resistor Capacitor Circuit
Dendrites

## Slide 15: NEUROMORPHIC ARCHITECTURES WITH DENDRITES
Active Dendrites with Calcium and NMDA channels: BrainScales
Floating-gate based active dendrites: Georgia Tech Neuron Chips
Dendrocentric Learning with multi-gate FeFETS (Boahen 2020)
DenRAM: Dendrites with Resistive RAM (Payvand 2024)
Dendrites have been modeled to different degrees in neuromorphic hardware.
Hodgkin Huxley Neurons with Active Dendrites
Ramakrishnan, 2013
NanoDendrite Multi-gate FeFET
Proposed Dendrite 3D Architecture
DenRAM with RRAM dendrites

## Slide 16: ACTIVE DENDRITES
Using shunting inhibition for gain modulation
peak input (A)
out (V)
Shunt Input
out
Excitatory Input
Raxial
Cleakage
Rleakage
Vmem
Vleakage
Vaxial

## Slide 17: DENDRITES FOR DIRECTION SELECTIVITY
Experimental Demonstration using analog circuits
Dendrite Circuit
Parker et. al IEEE ICONS 2024
FPAA 2.9V

## Slide 18: DENDRITES FOR DIRECTION SELECTIVITY
Dendrites for pattern and velocity estimation
w11
w12
w13
w21
w22
w23
wn1
wn2
wn3
Image Sensor (NXM pixels)
…
Super-Pixel
Feature Extraction
Complex
Features

## Slide 19: DRAGONFLY WITH DENDRITES
Using shunting inhibition for gain modulation
Original Dragonfly Interception Circuit (Chance 2020)
Dragonfly NN with Dendrites
Comparison with original interception circuit
Cardwell et al. In Review

## Slide 20: DendriteS in SPIKING NEURAL NETWORKS
Comparing networks with LIF and LIF +Dendrites
Chart: MSE Of LIF and Dendritic Networks
| MSE - SQRT | MSE - MISH
256 Hidden LIF | 0.0021469 | 0.0030814
16 Hidden LIF | 0.052921 | 0.0080707
16 Hidden Dendrite LIF | 0.0010934 | 0.0032298
256 / 16 Signals to LIF Neuron
16 Signals to LIF Neuron
Notes: To demonstrate SNN improvements we implemented a simple demonstration
Using examples from the SNN Torch library we trained MISH & SQRT - Mish is a newer activation function.
The dynamics of dendrites should embed more information reducing the needed communication across layers
We used:
A SNN with a hidden layer size of 256 LIF neurons - so the input is broadcast to 256 LIF neurons, which then send 256 spikes to an output neuron.
A 16x16 dendrite network. This consists of 16 dendrites with 16 inputs or taps each. This network sends 16 spikes to the LIF neuron
And as a comparison, a 16 LIF hidden layer network
The output of these networks is the last neuron's membrane potential.
We trained for 100 epochs, using a random sample of the function space .

## Slide 21: CO-DESIGN IS CHALLENGING
Software tools are critical for design and co-optimization
Materials/Device Design
Circuits/ System Design
Codesign
Application/ Algorithm Design
System Architecture Design

## Slide 22: DENDRITE ENABLED SPIKING NEURAL NETWORKS
Implemented a “Dendrite Pooling Layer” for use in ANN
Trained ResNet18 on CIFAR-10 for 300 epochs
  ResNet + Dendrite layer took significantly longer to train
  Simplified ODE layer adds state and loops
Found accuracy to be comparable
Dendritic pooling has potential in ANNs
Leveraging inherent properties of dendrites
Plagge et al., IEEE ICRC 2024
Pooling Layer Hardware | Energy
Digital Nvidia Jetson | 504.41 uJ
Dendritic pooling | 0.265 uJ

## Slide 23: DENDRITE ENABLED SPIKING NEURAL NETWORKS
Implemented Torch library with a dendritic chain
  Simplified version of the complex ODE dendrite solution.
  Wrapped dynamics into a set of constants and parameters.
Dendrites support SNNTorch & Non-Spiking Torch.
Provides a trainable 1-D chain of dendrites
Value | Type
Lambda | ”Spatial” constant: Represents Distance
Tau | “Temporal” constant: Capacitance and Resistance
Leak | Signal loss for each tap
Input Weight | Increases or Decreases signal strength
Learned Parameters
Hardware Constraints
Plagge et al., IEEE NICE 2024

## Slide 24: CHALLENGE: NOVEL CODESIGN TOOLS
  Rapidly estimate performance of neuromorphic architectures for design space exploration.
  General & extensible spiking H/W simulator
  Model functional behavior & track performance
  Schedule messages & intra-core interactions
  Calibrate simulator to real-world systems
  Accurately predicts latency & energy of gesture categorization spiking neural network (SNN)
SANA-FE: Specialized tool to explore novel neuromorphic architectures
SANA-FE: Simulating Advanced Neuromorphic Architectures for Fast Exploration
J. Boyle et al. ICONS 2023
Simulator Kernel
build architecture
initialize network
for all timesteps:
get external inputs
for all tiles:
for all cores:
process neuron
send messages
write results
Configuration & Input Spikes
Architecture Description
Performance Estimates
Mapped Spiking Neural Network

## Slide 25: DVS Gesture Recognition Application
Image reproduced from [Massa,’20]
Predict energy & performance for larger real-world neuromorphic applications
  SNN trained on DVS gesture data-set [Massa’20]
  18,678 neurons across 6 layers
  Mapped to 45 Loihi cores out of 128
Notes: Adapted and predicted energy for larger real-world applications such as hand gesture categorization of dynamic vision sensor data
Here predicted latency

## Slide 26: DVS Gesture Design Space Exploration
Design-space exploration using DVS gesture application
  Loihi-based designs, traded-off core count (c) vs neurons per core (n)
  Optimum design had 170 cores, 21% faster than Loihi (128 cores)
  Design-space sweep took 29 s
Image reproduced from [Massa,’20]

## Slide 27: Simulator Speed Results
Compared to existing discrete-event based spiking simulator (NeMo)
  Simulating IBM TrueNorth architecture
  Randomized SNN with 80% of spikes intra-core, 20% spikes between cores
Over 20x faster than NeMo for 1024 cores
Notes: Two things here
Modeling another spiking architecture TrueNorth (point to chip)
Compared against NeMo an existing TrueNorth simulator
  And shown that we are faster

## Slide 28: DENDRITES IN NEUROMORPHIC ARCHITECTURE
Further develop links with Dendrite-SNN hardware simulations – SanaFe
Work on a spiking self-attention network with dendrites:
  Dendritic attention layer (Temporal coherence and context)
  Dendritic pooling layers (More efficient summary layer)
Other compelling network designs
Release as stand-alone library or as SNNTorch add-on
An in-progress tool to estimate timing and energy of neuromorphic systems.
Currently supports Loihi.
Analog components are WIP
SanaFe – Hardware Simulator

## Slide 29: heterogeneous architectures
Move past general-purpose solutions and only use them for prototyping
Heterogeneous and reconfigurable systems
Get the best performance based on system needs.
System designed with application in mind for optimization
Near-sensor processing
Embracing Heterogeneity
‘Truly Heterogeneous Computing’,
Cardwell et al., SMC 2020

## Slide 30: APPLICATION SPECIFIC SOLUTIONS
We are in the ”golden-age of computer architectures”
Cui et al. arXiv 2024
Karki et al. Journal of Materials Research 2024
1
1
2
Hennessey &Patterson 2019
Notes: We took our neuromorphic approach and applied to a very different problem space

## Slide 31: PROBABILISTIC NEURAL SYSTEMS: COINFLIPS
OBJECTIVE: Leverage stochasticity in computing by exploiting the underlying physics of emerging random number generator (RNG) devices to build probabilistic neural architectures.
Collaborators: NYU, ORNL, Temple University, UT-Austin and UT-Knoxville, USA

## Slide 32: TRUE RANDOM NUMBER GENERATION (tRNG)
APPLICATION: HIGH ENERGY PHYSICS
Current PRNG Methods take 40—50% of CPU compute time.
TRNGs leveraging stochastic devices can lead to significant energy and latency savings.
RNG TODAY
Pierog et al., Phy Rev. 2022
COINFLIPS APPROACH
Expensive
Efficient
Misra et al., Adv. Materials 2022

## Slide 33: AI TO ACCELERATE CODESIGN FOR EMERGING COMPUTING
Computing demands are constantly increasing.
Emerging computing techniques can alleviate these challenges.
However, the design space is huge and optimization is needed across the stack.
AI-guided techniques can alleviate these challenges.
AI-Guided Tools a force multiplier for large design space
Application/ Algorithm Design
System Architecture Design
Materials/Device Design
Circuits/ System Design
AI-Guided Codesign
Misra et al., Adv. Materials 2022

## Slide 34: AI-GUIDED METHODS FOR EMERGING COMPUTING
EVOLUTIONARY OPTIMIZATION
Evolutionary algorithms
  LEAP: Library of Evolutionary Algorithms in Python
  EONS: Evolutionary Optimization for Neuromorphic Systems
REINFORCEMENT LEARNING
Trains agent to make optimal decisions in an environment to maximize rewards.
  Agent trained on PPO policy
  Environment: Physics-based Device model
Other AI Approaches: Physics-aware machine learning, Generative AI, Neural ODEs

## Slide 35: EA FOR CIRCUITS: MULTI-OBJECTIVE OPTIMIZATION
Multi-objective optimization of weights ω1, ω2, ω3 for optimal KL divergence and energy usage of MTJ-SHE devices
Kullback-Leibler
Divergence
Energy of a coinflip
Difference of weight from a fair coin
FITNESS FUNCTION
Cardwell et al., IEEE ICRC 2022
SHE: Spin Hall Effect

## Slide 36: REINFORCEMENT LEARNING FOR DEVICE CODESIGN
RL agent trained using PPO policy to find best device and material configuration.
Device validity checked.
Best configuration found normalizing for energy and KL-divergence.
Discover best device and material characteristics for TRNG
Metrics: Energy, KL Divergence
Device Check
Metric | Best Config
Energy (J) | 2.568x10-14
KL-Divergence | 0.0532
Cardwell et al., IEEE ISCAS 2024

## Slide 37: DEVICE PERFORMANCE TRADEOFFS
TRAINING RL AGENT
Agent had to balance both energy and KL-divergence for optimization which seemed to have an inverse relationship.
Reward schema is extremely important.
BENCHMARKING TRNGS
Comparing CMOS pRNG, tRNG, memristor tRNG and MTJ tRNG
Energy and KL-Divergence
Maicke et al., IOP Nano 2024
Cardwell et al., IEEE ISCAS 2024

## Slide 38: NEXT-GENERATION NEUROMORPHIC ARCHITECTURES
We need more dynamics and complexity per computational unit.
Leverage Stochasticity as a feature not a bug.
We need systems that do not just process, but can learn, adapt and reconfigure.
Novel integration: 3D architectures, wafer scale etc. for scaling and dense connectivity
Many areas where neuromorphic can have impact from HPC to edge.
Codesign tools can accelerate design space exploration and lead to creative solutions.
Re-think how we design computer architectures
Scientific
Computing
AI/ML
(ANN, SNN)
Brain-Inspired Algorithms
Edge
Computing
High Performance Computing
Probabilistic
Computing

## Slide 39: sgcardw@sandia.gov
Thank you!
Sandia National Laboratories
NEUROMORPHIC
https://neuroscience.sandia.gov/

## Slide 40: BACKUPS

## Slide 41: ATHENA (Analytical Tool to Evaluate Heterogeneous Neuromorphic Architectures)
  ATHENA will quickly evaluate performance metrics of analog architectures
  Developed as part of a larger ecosystem
    Tools to enable next-generation hardware design prototyping
Digital Accelerators
Novel Computing
Plagge et al., International Conference on Rebooting Computing (ICRC) 2022

## Slide 42: ATHENA – HARDWARE PERFORMANCE
ATHENA was used to compare the performance of multiple hardware devices against various deep learning networks
The SONOS tile-based architecture performed well across networks, with one notable exception: the Inception v3 network
This performance difference could be explored – showing ATHENA’s potential for codesign work
Plagge et al., International Conference on Rebooting Computing (ICRC) 2022

## Slide 43: ANN Network Applications – ResNet18
  Working with a graduate student intern at SNL
  Implemented a “Dendrite Pooling Layer” for use in AI ML
  Replaced traditional pooling layer with Dendrite Layer
  Trained ResNet18 on CIFAR-10 for 300 epochs
    ResNet + Dendrite layer took significantly longer to train
    Simplified ODE layer adds state and loops
  Found accuracy to be comparable
    Dendritic pooling has potential in ANNs
Chart: CIFAR10: ResNet18 / DendNet18 Accuracy 300 Epochs
| DendNet Validation Accuracy | ResNet Validation Accuracy
 | 0.85012 | 0.84703
Working with Priyam Mazumdar
Notes: To also demonstrate our library’s compatibility with Torch, we swapped the pooling layer in RESNET18 with dendrites
This work is in collaboration with Priyam Mazumdar a graduate intern SNL
We dubbed it "DendNet18", but the only difference is that the pooling layer was replaced with Dendrites in Torch.
We trained on CIFAR-10 for 300 epochs
And found validation accuracy to be comparable

## Slide 44: ML Network Applications – ResNet18
  ResNet18 – Was slower to train with a dendritic layer
    In hardware however, dendrites will be highly efficient
  Rough estimate of efficiency based on
    Energy =
      C = 10pF
      =2.5V
      = 100mV
    Nvidia Jetson values from Rodrigues, et. al
Pooling Layer on Digital Nvidia Jetson | 504.41 Micro Joules
Dendritic pooling | 0.265 Micro Joules
Rodrigues, Crefeda Faviola, Graham Riley, and Mikel Luján.
"Energy predictive models for convolutional neural networks on mobile platforms."
arXiv preprint arXiv:2004.05137 (2020).
Notes: Now we have some preliminary ideas as to how efficient these dendrites could be. In training, the network was significantly slower on GPU.
However - if we assume 140nm CMOS node size implementing dendrites:
Basic computation of a ResNet18 Pooling Layer
#Used ATHENA to compute energy