## Slide 1: Design, Code Generation, and Synthesis For the Next Generation Science Codes
Anshu Dubey
Argonne National Laboratory
Colloborators: Klaus Weide, Jared O'Neal , Johann Rudi, Youngjun Lee, Tom Klosterman, Wesley Kwiecinski, Mohamed Wahib
PPAM 2024

## Slide 2: Acknowledgements
This work was supported by the U.S. Department of Energy Office of Science, Office of Advanced Scientific Computing Research (ASCR), and by the Exascale Computing Project (17-SC-20-SC), a collaborative effort of the U.S. Department of Energy Office of Science and the National Nuclear Security Administration.
This work was performed in part at the Argonne National Laboratory, which is managed by UChicago Argonne, LLC for the U.S. Department of Energy under Contract No. DE-AC02-06CH11357

## Slide 3: Motivation
I hear this question often from domain scientists
  Should we even bother about porting when platforms are changing so much?
  Answer
    Can we afford not to – given that calculations do need to use leading edge platforms
    Shouldn’t we be thinking about how to design our code so that we are nimble in tuning performance
That gives rise to the question – can we
  Here is one attempt to argue that we can
  Fairly confident that this will work for many classes of PDE based applications
  For others --- similar methodology in approaching design challenges might work

## Slide 4: Research Software Challenges
Many parts of the model and software system can be under research
Requirements change throughout the lifecycle as knowledge grows
Verification complicated by floating point representation
Real world is messy
More Scientific Understanding
Higher Fidelity
Model
More Diverse
Solvers
More Hardware
Resources

## Slide 5: It Gets Worse
More Scientific Understanding
Higher Fidelity
Model
More Diverse
Solvers
More Hardware
Resources
AI in the mix

## Slide 6: Design Considerations And Their Implications
Considerations
Multidisciplinary
  Many facets of knowledge
  To know everything is not feasible
Two types of code components
  Infrastructure (mesh/IO/runtime …)
  Science models (numerical methods)
Codes grow
  New ideas => new features
  Code reuse by others
Design Implications
Separation of Concerns
  Shield developers from unnecessary complexities
Work with different lifecycles
  Long-lasting vs quick changing
  Logically vs mathematically complex
Extensibility built in
  Ease of adding new capabilities
  Customizing existing capabilities

## Slide 7: State of Practice – Abstractions and Runtimes
Still very focused on GPU
  Majority of ECP applications park their data on the GPU and just work there
What are the abstractions ---
  Data structure libraries (Kokkos) and parallelization of loops
    Parallel for / do concurrent etc
Limitations
  No way to handle algorithmic variants in a unified way
  Getting hard-baked into C++
    by no means the best designed language for scientific computations
  No way to transfer domain knowledge based possible optimizations to the tools
None of the prevalent languages allow a good way to define data locality
  Boutique HPC languages like chapel do – but chicken and egg problem with adoption
So shall we throw up our hands and say computational science is doomed, let’s just find some other way of advancing science?
Or is there a way?

## Slide 8: State of Practice – Abstractions and Runtimes
Still very focused on GPU
  Majority of ECP applications park their data on the GPU and just work there
What are the abstractions ---
  Data structure libraries (Kokkos) and parallelization of loops
    Parallel for / do concurrent etc
Limitations
  No way to handle algorithmic variants in a unified way
  Getting hard-baked into C++ -- by no means the best designed language for scientific computations
  No way to transfer domain knowledge based possible optimizations to the tools
None of the prevalent languages allow a good way to define data locality
  Boutique HPC languages like chapel do – but chicken and egg problem with adoption
So shall we throw up our hands and say computational science is doomed, let’s just find some other way of advancing science?
Or is there a way?
We have been developing one for Flash-X using abstractions, code synthesis and code generation

## Slide 9: Mechanisms Needed by the Code
Mechanisms to unify expression of computation
Minimize maintained variants of source suitable for all computational devices
Reconcile differences in data structures

## Slide 10: Mechanisms Needed by the Code
Mechanisms to map work to computational targets
Figuring out the map
  Expression of dependencies
  Cost models
Expressing the map
Mechanisms to unify expression of computation
Minimize maintained variants of source suitable for all computational devices
Reconcile differences in data structures

## Slide 11: Mechanisms Needed by the Code
Mechanisms to map work to computational targets
Figuring out the map
  Expression of dependencies
  Cost models
Expressing the map
Mechanisms to move work and data to computational targets
Moving between devices
  Launching work at the destination
  Hiding latency of movement
Moving data off node
Mechanisms to unify expression of computation
Minimize maintained variants of source suitable for all computational devices
Reconcile differences in data structures

## Slide 12: Mechanisms Needed by the Code
Mechanisms to map work to computational targets
Figuring out the map
  Expression of dependencies
  Cost models
Expressing the map
Mechanisms to move work and data to computational targets
Moving between devices
  Launching work at the destination
  Hiding latency of movement
Moving data off node
Mechanisms to unify expression of computation
Minimize maintained variants of source suitable for all computational devices
Reconcile differences in data structures
So, what do we need?
Composable components
Code synthesis tools
Code generation tools
Data movement orchestrator

## Slide 13: Composability
setup
Encoded metadata
Components I need
Components I don’t work with
State variables I need
AMR specific needs
Runtime parameters I want …
Alternative
Implementations
Config files
Sub components
Building blocks of code
  Hierarchy of granularity
  Units, subunits, components
Multiple alternative implementations
  Null implementations of API
  High degree of composability
  High degree of customizability
Self describing

## Slide 14: Philosophy of Design
Let the code developer decide what should be done for optimization on a platform
  Make it easy to have that happen without coding to metal
Have a set of tools, each with limited functionality
  Tools remain simple and easy to maintain by non-experts
  Combination of tools provides a powerful solution
Tools can permute and combine building blocks, do some code translation and compose a full application
As far as possible tools also have building blocks

## Slide 15: Orthogonal Axes of Challenges and Optimization
  Separate out arithmetic and control flow
    Make arithmetic invariant
    Turn separate pieces into building blocks using macros
[hy_fluxesSec1]
args= XL, XR,limits
definition =
@M loop_begin(limits)
if (flux(1@M indices) > 0.) then
call doSection1(XL(:@M indices), ……)
else
call doSection1(XR(:@M indices), …….)
end if
@M loop_end
Permit alternative definitions for all the macros as needed
Build in arbitration mechanism for picking the right definition
This code section can be invoked as
  @M hy_fluxesSec1(uLeft,uRight,blkLimits)
Alternative Definitions
For all spatial points at once For one spatial point at a time
[indices] [indices]
definition = definition =
,i,j,k
[loop_begin] [loop_begin]
args = limits args = limits
definition= definition=
do k = limits(LOW,KAXIS),limits(LOW,KAXIS)
do j = limits(LOW,JAXIS),limits(LOW,JAXIS)
do I = limits(LOW,IAXIS),limits(LOW,IAXIS)
[loop_end] [loop_end]
definition = definition =
enddo
enddo
enddo

## Slide 16: Alternatively
  With macros it is possible to use any arbitrary code section as a building block
[hy_fluxesSec1]
args= XL, XR,limits
definition =
@M loop_begin(limits)
if (flux(1@M indices) > 0.) then
@M doSection1(XL)
else
@M doSection1(XR)
end if
@M loop_end
[doSection1]
args=uDir
definition =
… some computation
uDir(:@M indices) = res
Alternative Definitions
For all spatial points at once For one spatial point at a time
[indices] [indices]
definition = definition =
,i,j,k
[loop_begin] [loop_begin]
args = limits args = limits
definition= definition=
do k = limits(LOW,KAXIS),limits(LOW,KAXIS)
do j = limits(LOW,JAXIS),limits(LOW,JAXIS)
do I = limits(LOW,IAXIS),limits(LOW,IAXIS)
[loop_end] [loop_end]
definition = definition =
enddo
enddo
enddo

## Slide 17: Orthogonal Axes of Challenges and Optimization
We have moved binding of data structure to configuration phase from the development phase – not compilation phase
Another utility reorders indices
Between them, without changing code one can explore performance options

## Slide 18: Orthogonal Axes of Challenges and Optimization
We have moved binding of data structure to configuration phase from the development phase – not compilation phase
Another utility reorders indices
Between them, without changing code one can explore performance options
Here we combine composition and synthesis with building blocks

## Slide 19
Orthogonal Axes of Challenges and Optimization
  Have a method for expressing algorithmic variants
    Without delving into the details of the arithmetic
Example -- Flash-X supports two block-structured AMR grid backends
  Paramesh: Octree-based, AMReX: Level-based
Each has different preferences for flux correction at fine-coarse boundaries
For higher order RK integration Communication avoidance – telescoping mode

## Slide 20
Orthogonal Axes of Challenges and Optimization
  Have a way of rearranging data locality and moving data and computation
    Let the human-in-the-loop dictate this
CG-Kit – recipes in python
-- templates for different variants
-- express where to compute what
-- emit code in Fortran/C/C++
Milhoja – flatten/decompose data and move it to the target
-- combine multiple units into one packet
-- decompose into smaller units if needed
Insights
If tools only execute what they are told to, they are simpler
  Analysis and inferencing is hard – reason why there are no magic compilers
Code generation is our friend – especially when it is simple forward map
  And is not entangled with the details of the arithmetic

## Slide 21: CGkit
Generating Code from Recipes and code Templates
Source Tree Tool
Control Flow Tool
Recipe Tool
( Parser)
recipes written by humans
templates (FORTRAN or C/C++)
source code for time stepping
Example recipe
Resulting control flow graph
express dependen-
cies
express hardware mapping
Orthogonal separation of concerns

## Slide 22: Parametrized Source Tree (PST)
PST represents source codes in a tree topology based on:
  Source code
  Parameters
  Links / Connectors

## Slide 23: Spark Variants

## Slide 24: Milhoja and Code Generation
R
S
Task Fcn B (GPU)
X
Y
Task Fcn A (CPU)
T
Task Fcn C (CPU)
Z
CPU
CPU
Distributor
DM/Unpack
Data Packet
ConcurrentDataBegin
ConcurrentDataEnd
Packing and unpacking
If N blocks are sent to the device we need N copies of all blockwise scratch
For all data items we need device pointers
Code internally decorated with directives

## Slide 25: Code Generators
Two Classes
  Data packet generators
    Parse the interface files
    Collect all data to be put into a data packet
    Generate code that will flatten all data into data packets
  Task function generators
    Consolidate functions to be invoked
    Bookended by internode communication
    Unpack data packets
Decorate interface definitions with needed metadata
    Example

## Slide 26: Code generation
CG-Kit PST Templates
CG-Kit Recipe
Platform-specific knowledge
Control Flow Graph
Control Flow Graph & PST
JSON generator
Milhoja
(code generator)
Generated Source code
(Data Packets & Taskfunctions)
Generated Source code
(Time Stepper)
Static source codes (Fortran or C/C++)
Configuration and arbitration
Fully assembled source code
Compiler
Platform-specific executable
Milhoja
(runtime)
(Numerics & Macros)
What the
Physicists
Code
Macro translation

## Slide 27: Code generation
CG-Kit PST Templates
CG-Kit Recipe
Platform-specific knowledge
Control Flow Graph
Control Flow Graph & PST
JSON generator
Milhoja
(code generator)
Generated Source code
(Data Packets & Taskfunctions)
Generated Source code
(Time Stepper)
Static source codes (Fortran or C/C++)
Configuration and arbitration
Fully assembled source code
Compiler
Platform-specific executable
Milhoja
(runtime)
(Numerics & Macros)
What the
Physicists
Code
What is expected from them –
Enumeration of all data to be managed in the form of comments in the interface in specified syntax
All allocations registered with the tools
All data either transferred as arguments, or be block invariant
Macro translation

## Slide 28: Spark Variants (RK Modes)
Performance comparisons on the CPU-only machine (Fugaku)
Performance comparisons on the GPU
(Nvidia RTX 3080)

## Slide 29: Advantage of Orchestrating
Offloading performance of Hydro 2D
Offloading performance of Hydro 3D

## Slide 30: Porting to a new platform
In an ideal world
  Add to the library of runtime pipelines
  Add to the library of recipes templates
In real world
  Add variants for some solvers with alternative definitions of macros
In the worst case
  Develop new algorithms and add whole alternative implementation for some solvers

## Slide 31: References
Dubey, Anshu, et al. "Flash-X: A multiphysics simulation software instrument." SoftwareX 19 (2022): 101168.
Rudi, Johann, et al. "CG-Kit: Code Generation Toolkit for Performant and Maintainable Variants of Source Code Applied to Flash-X Hydrodynamics Simulations." arXiv preprint arXiv:2401.03378 (2024), accepted for Future Generation Computer Systems
O’Neal, Jared, et al. "Domain-specific runtime to orchestrate computation on heterogeneous platforms." European Conference on Parallel Processing. Cham: Springer International Publishing, 2021.
Dubey, Anshu, et al. "A tool and a methodology to use macros for abstracting variations in code for different computational demands." Future Generation Computer Systems (2023).